## Slide 1: Campus Network Design Workshop
Layer 2 Engineering –
Spanning Tree and VLANs
This document is a result of work by the Network Startup Resource Center (NSRC at http://www.nsrc.org). This document may be freely copied, modified, and otherwise re-used on the condition that any re-use acknowledge the NSRC as the original source.

## Slide 2: Switching Loop
Switch A
Switch B
Switch C
When there is more than one path between two switches
What are the potential problems?

## Slide 3: Switching Loop
If there is more than one path between two switches:
  Forwarding tables become unstable
    Source MAC addresses are repeatedly seen coming from different ports
  Switches will broadcast each other’s broadcasts
    All available bandwidth is utilized
    Switch processors cannot handle the load

## Slide 4: Switching Loop
Switch A
Switch B
Switch C
Node1 sends a broadcast frame (e.g. an ARP request)
Node 1

## Slide 5: Switching Loop
Switch A
Switch B
Switch C
Switches A, B and C broadcast node 1’s frame out every port
Node 1

## Slide 6: Switching Loop
Switch A
Switch B
Switch C
But they receive each other’s broadcasts, which they need to forward again out every port!
The broadcasts are amplified, creating a broadcast storm
Node 1

## Slide 7: Good Switching Loops
But you can take advantage of loops!
  Redundant paths improve resilience when:
    A switch fails
    Wiring breaks
How to achieve redundancy without creating dangerous traffic loops?

## Slide 8: What is a Spanning Tree?
“Given a connected, undirected graph, a spanning tree of that graph is a subgraph which is a tree and connects all the vertices together”.
A single graph can have many different spanning trees.

## Slide 9: Spanning Tree Protocol
The purpose of the protocol is to have bridges dynamically discover a subset of the topology that is loop-free (a tree) and yet has just enough connectivity so that where physically possible, there is a path between every switch

## Slide 10: Spanning Tree Protocol
Several flavors:
  Traditional Spanning Tree (802.1d)
  Rapid Spanning Tree or RSTP (802.1w)
  Multiple Spanning Tree or MSTP (802.1s)

## Slide 11: Traditional Spanning Tree (802.1d)
Switches exchange messages that allow them to compute the Spanning Tree
  These messages are called BPDUs (Bridge Protocol Data Units)
  Two types of BPDUs:
    Configuration
    Topology Change Notification (TCN)

## Slide 12: Traditional Spanning Tree (802.1d)
First Step:
  Decide on a point of reference: the Root Bridge
  The election process is based on the Bridge ID, which is composed of:
    The Bridge Priority: A two-byte value that is configurable
    The MAC address: A unique, hardcoded address that cannot be changed.

## Slide 13: Root Bridge Selection (802.1d)
Each switch starts by sending out BPDUs with a Root Bridge ID equal to its own Bridge ID
  I am the root!
Received BPDUs are analyzed to see if a lower Root Bridge ID is being announced
  If so, each switch replaces the value of the advertised Root Bridge ID with this new lower ID
Eventually, they all agree on who the Root Bridge is

## Slide 14: Root Bridge Selection (802.1d)
Switch B
Switch C
Switch A
32768.0000000000AA
32768.0000000000BB
32768.0000000000CC
All switches have the same priority.
Who is the elected root bridge?

## Slide 15: Root Port Selection (802.1d)
Now each switch needs to figure out where it is in relation to the Root Bridge
  Each switch needs to determine its Root Port
  The key is to find the port with the lowest Root Path Cost
    The cumulative cost of all the links leading to the Root Bridge

## Slide 16: Root Port Selection (802.1d)
Each link on a switch has a Path Cost
  Inversely proportional to the link speed
    e.g. The faster the link, the lower the cost
Link Speed | STP Cost
10 Mbps | 100
100 Mbps | 19
1 Gbps | 4
10 Gbps | 2

## Slide 17: Root Port Selection (802.1d)
Root Path Cost is the accumulation of a link’s Path Cost and the Path Costs learned from neighboring Switches.
  It answers the question: How much does it cost to reach the Root Bridge through this port?

## Slide 18: Root Port Selection (802.1d)
Root Bridge sends out BPDUs with a Root Path Cost value of 0
Neighbor receives BPDU and adds port's Path Cost to Root Path Cost received
Neighbor sends out BPDUs with new cumulative value as Root Path Cost
Other neighbors down the line keep adding in the same fashion

## Slide 19: Root Port Selection (802.1d)
On each switch, the port where the lowest Root Path Cost was received becomes the Root Port
  This is the port with the best path to the Root Bridge

## Slide 20: Root Port Selection (802.1d)
Switch B
Switch C
Switch A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32768.0000000000AA
32768.0000000000BB
32768.0000000000CC
What is the Path Cost on each Port?
What is the Root Port on each switch?

## Slide 21: Root Port Selection (802.1d)
Switch B
Switch C
Switch A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32768.0000000000AA
32768.0000000000BB
32768.0000000000CC
Root Port
Root Port

## Slide 22: Electing Designated Ports (802.1d)
OK, we now have selected root ports but we haven’t solved the loop problem yet, have we
  The links are still active!
Each network segment needs to have only one switch forwarding traffic to and from that segment
Switches then need to identify one Designated Port per network segment
  The one with the lowest cumulative Root Path Cost to the Root Bridge

## Slide 23: Electing Designated Ports (802.1d)
Two or more ports in a segment having identical Root Path Costs is possible, which results in a tie condition
All STP decisions are based on the following sequence of conditions:
  Lowest Root Bridge ID
  Lowest Root Path Cost to Root Bridge
  Lowest Sender Bridge ID
  Lowest Sender Port ID

## Slide 24: Electing Designated Ports (802.1d)
Which port should be the Designated Port on each segment?
Switch B
Switch C
Switch A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32768.0000000000AA
32768.0000000000BB
32768.0000000000CC

## Slide 25: Electing Designated Ports (802.1d)
Switch B
Switch C
Switch A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32768.0000000000AA
32768.0000000000BB
32768.0000000000CC
Designated Port
Designated Port
Designated Port
In the B-C link, Switch B has the lowest Bridge ID, so port 2 in Switch B is the Designated Port

## Slide 26: Blocking a port
Any port that is not elected as either a Root Port, nor a Designated Port is put into the Blocking State.
This step effectively breaks the loop and completes the Spanning Tree.

## Slide 27: Designated Ports on each segment (802.1d)
Port 2 in Switch C is then put into the Blocking State because it is neither a Root Port nor a Designated Port
Switch B
Switch C
Switch A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32768.0000000000AA
32768.0000000000BB
32768.0000000000CC
✕

## Slide 28: Spanning Tree Protocol States
Disabled
  Port is shut down
Blocking
  Not forwarding frames
  Receiving BPDUs
Listening
  Not forwarding frames
  Sending and receiving BPDUs

## Slide 29: Spanning Tree Protocol States
Learning
  Not forwarding frames
  Sending and receiving BPDUs
  Learning new MAC addresses
Forwarding
  Forwarding frames
  Sending and receiving BPDUs
  Learning new MAC addresses

## Slide 30: STP Topology Changes
Switches will recalculate if:
  A new switch is introduced
    It could be the new Root Bridge!
  A switch fails
  A link fails

## Slide 31: Root Bridge Placement
Using default STP parameters might result in an undesired situation
  Traffic will flow in non-optimal ways
  An unstable or slow switch might become the root
You need to plan your assignment of bridge priorities carefully

## Slide 32: Bad Root Bridge Placement
Switch D
Switch C
Switch B
32768.0000000000BB
32768.0000000000DD
32768.0000000000CC
Switch A
32768.0000000000AA
Root Bridge
Out to router

## Slide 33: Good Root Bridge Placement
Switch D
Switch C
Switch B
16384.0000000000BB
12288.0000000000DD
32768.0000000000CC
Switch A
32768.0000000000AA
Alernative Root Bridge
Out to active router
Root Bridge
Out to standby router

## Slide 34: Protecting the STP Topology
Some vendors have included features that protect the STP topology:
  Root Guard
  BPDU Guard
  Loop Guard
  UDLD
  Etc.

## Slide 35: STP Design Guidelines
Enable spanning tree even if you don’t have redundant paths
Always plan and set bridge priorities
  Make the root choice deterministic
  Include an alternative root bridge
If possible, do not accept BPDUs on end user ports
  Apply BPDU Guard or similar where available

## Slide 36: 802.1d Convergence Speeds
Moving from the Blocking state to the Forwarding State takes at least 2 x Forward Delay time units (~ 30 secs.)
  This can be annoying when connecting end user stations
Some vendors have added enhancements such as PortFast, which will reduce this time to a minimum for edge ports
  Never use PortFast or similar in switch-to-switch links
Topology changes typically take 30 seconds too
  This can be unacceptable in a production network

## Slide 37: Rapid Spanning Tree (802.1w)
Convergence is much faster
  Communication between switches is more interactive
Edge ports don’t participate
  Edge ports transition to forwarding state immediately
  If BPDUs are received on an edge port, it becomes a non-edge port to prevent loops

## Slide 38: Rapid Spanning Tree (802.1w)
Defines these port roles:
  Root Port (same as with 802.1d)
  Alternate Port
    A port with an alternate path to the root
  Designated Port (same as with 802.1d)
  Backup Port
    A backup/redundant path to a segment where another bridge port already connects.

## Slide 39: Rapid Spanning Tree (802.1w)
Synchronization process uses a handshake method
  After a root is elected, the topology is built in cascade, where each switch proposes to be the designated bridge for each point-to-point link
  While this happens, all the downstream switch links are blocking

## Slide 40: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP

## Slide 41: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP
DP
RP

## Slide 42: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP
DP
RP
DP
RP

## Slide 43: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP
DP
RP
DP
RP
DP
RP

## Slide 44: Rapid Spanning Tree (802.1w)
Prefer RSTP over STP if you want faster convergence
Always define which ports are edge ports

## Slide 45: Questions?

## Slide 46: Virtual LANs (VLANs)
Allow us to split switches into separate (virtual) switches
Only members of a VLAN can see that VLAN’s traffic
  Inter-vlan traffic must go through a router
Allow us to reuse router interfaces to carry traffic for separate subnets
  E.g. sub-interfaces in Cisco routers

## Slide 47: Local VLANs
2 VLANs or more within a single switch
Edge ports, where end nodes are connected, are configured as members of a VLAN
The switch behaves as several virtual switches, sending traffic only within VLAN members

## Slide 48: Local VLANs
VLAN X
VLAN Y
Switch
VLAN X nodes
VLAN Y nodes
Edge ports

## Slide 49: VLANs across switches
Two switches can exchange traffic from one or more VLANs
Inter-switch links are configured as trunks, carrying frames from all or a subset of a switch’s VLANs
Each frame carries a tag that identifies which VLAN it belongs to

## Slide 50: 802.1Q
The IEEE standard that defines how ethernet frames should be tagged when moving across switch trunks
This means that switches from different vendors are able to exchange VLAN traffic.

## Slide 51: 802.1Q tagged frame

## Slide 52: VLANs across switches
802.1Q Trunk
Tagged Frames
VLAN X
VLAN Y
VLAN X
VLAN Y
Edge Ports
Trunk Port
This is called “VLAN Trunking”

## Slide 53: Tagged vs. Untagged
Edge ports are not tagged, they are just “members” of a VLAN
You only need to tag frames in switch-to-switch links (trunks), when transporting multiple VLANs
A trunk can transport both tagged and untagged VLANs
  As long as the two switches agree on how to handle those

## Slide 54: VLANs increase complexity
You can no longer “just replace” a switch
  Now you have VLAN configuration to maintain
  Field technicians need more skills
You have to make sure that all the switch-to-switch trunks are carrying all the necessary VLANs
  Need to keep in mind when adding/removing VLANs

## Slide 55: Good reasons to use VLANs
You want to segment your network into multiple subnets, but can’t buy enough switches
  Hide sensitive infrastructure like IP phones, building controls, etc.
Separate control traffic from user traffic
  Restrict who can access your switch management address

## Slide 56: Bad reasons to use VLANs
Because you can, and you feel cool 
Because they will completely secure your hosts (or so you think)
Because they allow you to extend the same IP network over multiple separate buildings
  This is actually very common, but a bad idea

## Slide 57: Do not build “VLAN spaghetti”
Extending a VLAN to multiple buildings across trunk ports
Bad idea because:
  Broadcast traffic is carried across all trunks from one end of the network to another
  Broadcast storm can spread across the extent of the VLAN, and affect all VLANS!
  Maintenance and troubleshooting nightmare

## Slide 58: Link Aggregation
Also known as port bundling, link bundling
You can use multiple links in parallel as a single, logical link
  For increased capacity
  For redundancy (fault tolerance)
LACP (Link Aggregation Control Protocol) is a standardized method of negotiating these bundled links between switches

## Slide 59: LACP Operation
Two switches connected via multiple links will send LACPDU packets, identifying themselves and the port capabilities
They will then automatically build the logical aggregated links, and then pass traffic.
Switch ports can be configured as active or passive

## Slide 60: LACP Operation
Switch A
Switch B
LACPDUs
Switches A and B are connected to each other using two sets of Fast Ethernet ports
LACP is enabled and the ports are turned on
Switches start sending LACPDUs, then negotiate how to set up the aggregation
100 Mbps
100 Mbps

## Slide 61: LACP Operation
200 Mbps logical link
The result is an aggregated 200 Mbps logical link
The link is also fault tolerant: If one of the member links fail, LACP will automatically take that link off the bundle, and keep sending traffic over the remaining link
Switch A
Switch B
100 Mbps
100 Mbps

## Slide 62: Distributing Traffic in Bundled Links
Bundled links distribute frames using a hashing algorithm, based on:
  Source and/or Destination MAC address
  Source and/or Destination IP address
  Source and/or Destination Port numbers
This can lead to unbalanced use of the links, depending on the nature of the traffic
Always choose the load-balancing method that provides the most distribution

## Slide 63: Questions?

## Slide 64: Multiple Spanning Tree (802.1s)
Allows separate spanning trees per VLAN group
  Different topologies allow for load balancing between links
  Each group of VLANs are assigned to an “instance” of MST
Compatible with STP and RSTP

## Slide 65: Multiple Spanning Tree (802.1s)
Vlan A
Vlan B
Root VLAN A
Root VLAN B
✕
✕

## Slide 66: Multiple Spanning Tree (802.1s)
MST Region
  Switches are members of a region if they have the same set of attributes:
    MST configuration name
    MST configuration revision
    Instance-to-VLAN mapping
  A digest of these attributes is sent inside the BPDUs for fast comparison by the switches
  One region is usually sufficient

## Slide 67: Multiple Spanning Tree (802.1s)
CST = Common Spanning Tree
  In order to interoperate with other versions of Spanning Tree, MST needs a common tree that contains all the other islands, including other MST regions

## Slide 68: Multiple Spanning Tree (802.1s)
IST = Internal Spanning Tree
  Internal to the Region, that is
  Presents the entire region as a single virtual bridge to the CST outside

## Slide 69: Multiple Spanning Tree (802.1s)
MST Instances
  Groups of VLANs are mapped to particular Spanning Tree instances
  These instances will represent the alternative topologies, or forwarding paths
  You specify a root and alternate root for each instance

## Slide 70: Multiple Spanning Tree (802.1s)
CST
MST Region
IST
MST Region
IST
802.1D switch

## Slide 71: Multiple Spanning Tree (802.1s)
Design Guidelines
  Determine relevant forwarding paths, and distribute your VLANs equally into instances matching these topologies
  Assign different root and alternate root switches to each instance
  Make sure all switches match region attributes
  Do not assign VLANs to instance 0, as this is used by the IST

## Slide 72: Selecting Switches
Minimum features:
  Standards compliance
  Encrypted management (SSH/HTTPS)
  VLAN trunking
  Spanning Tree (RSTP at least)
  SNMP
    At least v2 (v3 has better security)
    Traps

## Slide 73: Selecting Switches
Other recommended features:
  DHCP Snooping
    Prevent end-users from running a rogue DHCP server
      Happens a lot with little wireless routers (Netgear, Linksys, etc) plugged in backwards
    Uplink ports towards the legitimate DHCP server are defined as “trusted”. If DHCPOFFERs are seen coming from any untrusted port, they are dropped.

## Slide 74: Selecting Switches
Other recommended features:
  Dynamic ARP inspection
    A malicious host can perform a man-in-the-middle attack by sending gratuitous ARP responses, or responding to requests with bogus information
    Switches can look inside ARP packets and discard gratuitous and invalid ARP packets.

## Slide 75: Selecting Switches
Other recommended features:
  IGMP Snooping:
    Switches normally flood multicast frames out every port
    Snooping on IGMP traffic, the switch can learn which stations are members of a multicast group, thus forwarding multicast frames only out necessary ports
    Very important when users run Norton Ghost, for example.

## Slide 76: Network Management
Enable SNMP traps and/or syslog
  Collect and process in centralized log server
    Spanning Tree Changes
    Duplex mismatches
    Wiring problems
Monitor configurations
  Use RANCID to report any changes in the switch configuration

## Slide 77: Network Management
Collect forwarding tables with SNMP
  Allows you to find a MAC address in your network quickly
  You can use simple text files + grep, or a web tool with DB backend
Enable LLDP (or CDP or similar)
  Shows how switches are connected to each other and to other network devices

## Slide 78: Documentation
Document where your switches are located
  Name switch after building name
    E.g. building1-sw1
  Keep files with physical location
    Floor, closet number, etc.
Document your edge port connections
  Room number, jack number, server name

## Slide 79: Questions? This document is a result of work by the Network Startup Resource Center (NSRC at http://www.nsrc.org). This document may be freely copied, modified, and otherwise re-used on the condition that any re-use acknowledge the NSRC as the original source.